## Slide 1: ENGI 301 Putting Speed Control Device Proposal
10/4/2020
Grace Wilson

## Slide 2: Background Information
A device that measures the speed at which a golf ball approaches the hole. It will be positioned directly in front of the cup, but out of the line of the putt. Used on flat putting surfaces to help with speed/distance control.
The device will provide visual and audible feedback. The ball speed will be visible on a small display screen, and a speaker will inform the user of the quality of the putt based on its speed:
  Slow speeds: ”Barely got there!”
  Fast speeds: “A little strong!”
  Perfect speed: “Perfect putt!”
The device will utilize IR sensors, a screen display, a speaker, and the Pocket Beagle to achieve this functionality.
The screen will display a short history of the speeds of the last four putts, and the device will be powered on and off with a power button

## Slide 3: Rough Sketch of Device Design

## Slide 4: Existing Solutions
There are a few existing projects that use an Arduino UNO to detect the speed of toy cars passing in front of an IR sensor set up. The projects are linked below:
  https://www.hackster.io/yashastronomy/arduino-speed-detector-4eab71
  https://www.hackster.io/embeddedlab786/car-speed-detector-d60ea0
  https://www.hackster.io/NerdFatherRJ/speeduino-speed-tracker-c8fcae
The improvements that will be made are an added audible component to the device. This audio feedback will allow users to understand the device’s analysis of the putt without relocating from their putting position to check the display screen. Additionally, a PocketBeagle will be used instead of an Arduino.

## Slide 5: System Block Diagram
PocketBeagle
GPIO58/P2_4
GPIO57/P2_6
GPIO60/P2_8
I2C1 SCL/P2_9
IR Proximity Sensor 1:
GP2Y0A21YK0F
IR Proximity Sensor 2:
GP2Y0A21YK0F
Power Button
20x4 I2C Character LCD Display:
CFAH2004AC-TMI-EW
USB to Audio Jack
USB1
I2C1 SDA/P2_11
Micro USB Power
USB0

## Slide 6: Power Block Diagram
PocketBeagle
IR Proximity Sensor 1:
~ 30mA
IR Proximity Sensor 2:
~ 30 mA
Power Button:
up to 50 mA
20x4 I2C Character LCD Display:
up to 1.5 mA
USB to Audio Jack
5V
5V
5V
3.3V
5V
SYS_VOUT
3.3V_VOUT
VIN_USB1
SYS_VOUT
SYS_VOUT
Micro USB Power
5V
VIN_USB0

## Slide 7: Components/Budget
Component | Need to Buy | Cost
Sharp IR Analog Distance Sensors: https://www.pololu.com/product/136 | x2 | $10.29
20x4 I2C Character LCD Display: https://www.crystalfontz.com/product/cfah2004actmiew-20x4-i2c-character-lcd?kw=&origin=pla&gclid=CjwKCAjwq_D7BRADEiwAVMDdHiHPBFW64CMppy-nCaKe0sCETMsAPY2SlfEIacJEAEYCOHrj1hV69BoCuvgQAvD_BwE#undefined | x1 | $15.81
USB to Audio Jack | No | 
Button for Powering on Device | No |