## Slide 1: ENGI 301 Putting Speed Control Device Proposal
10/4/2020
Grace Wilson

## Slide 2: Background Information
A device that measures the speed at which a golf ball approaches the hole. It will be positioned directly in front of the cup, slightly offset from the line of the putt. Used on flat putting surfaces to help with speed/distance control.
The device will provide visual and audible feedback. The ball speed will be visible on a small display screen, and a speaker will inform the user of the quality of the putt based on its speed:
  Slow speeds: ”Too slow!”
  Fast speeds: “Too fast!”
  Perfect speed: “Perfect putt!”
The device will utilize IR sensors, a screen display, a speaker, buttons, and the Pocket Beagle to achieve this functionality.
The screen will display a history of the speeds of the recorded putts, and two buttons will be used to scroll up and down the list of putt speeds. All speeds are in cm/s

## Slide 3: System Block Diagram
PocketBeagle
GPIO26/P1_34
GPIO87/P1_2
GPIO20/P1_20
I2C1 SCL/P2_9
IR Proximity Sensor 1:
GP2Y0A21YK0F
IR Proximity Sensor 2:
GP2Y0A21YK0F
Record Button
20x4 I2C Character LCD Display:
CFAH2004AC-TMI-EW
USB to Audio Jack
USB1
I2C1 SDA/P2_11
Micro USB Power
USB0
PRU0.1/P1_33
History Button
GPIO52/P2_10
Toggle Up Button
Toggle Down Button
GPIO27/P2_19

## Slide 4: Power Block Diagram
PocketBeagle
IR Proximity Sensor 1:
~ 30mA
IR Proximity Sensor 2:
~ 30 mA
Buttons:
up to 50 mA
20x4 I2C Character LCD Display:
up to 1.5 mA
USB to Audio Jack
5V
5V
5V
5V
SYS_VOUT
3.3V_VOUT
VIN_USB1
SYS_VOUT
SYS_VOUT
Micro USB Power
5V
VIN_USB0
1k ohm R
1k ohm R
1k ohm R
SYS_VOUT
SYS_VOUT
SDA
SCL
5V
5V
3.3V

## Slide 5
Mechanical Block Diagram
LCD Display
Pocket Beagle
History Button
Record Button
Scroll Button
Scroll Button
USB for Audio
Sensor 1
Sensor 2
FRONT
BACK
5.9”
2.7"